## Slide 1
Engineering · EyobuNjineli · Ingenieurswese
Photo by Stefan Els
Real-time 3D Biomechanical Analysis and AI Personal Trainer for Strength And Conditioning Exercises Using Markerless Motion Capture
Rensu P Theart, Lizé Steyn, Keagan Ellenberger, Chris-Mari Schreuder
Notes: Good [morning/afternoon], today I’ll present work on real-time 3D biomechanical analysis and an AI personal trainer using markerless motion capture. This is based on Masters work I supervised, conducted by Lize Steyn

## Slide 2
Engineering · EyobuNjineli · Ingenieurswese
Current Limitations in Motion Analysis
  Traditional 3D motion capture systems are expensive
  Require specialised laboratory environments
  Limited accessibility for athletes and trainers
  The gap between research-grade analysis and practical application
Notes: “Traditional 3D motion capture is accurate but expensive, needs labs, and is not accessible to gyms or athletes. Our goal: close the gap between research-grade analysis and practical, affordable tools.”

## Slide 3
Engineering · EyobuNjineli · Ingenieurswese
Markerless Motion Capture System
  Our System Requirements
  Real-time 3D biomechanical feedback
  Low-cost webcam setup (3 cameras)
  No markers or specialized equipment required
  Accessible for gyms, clinics, and home use
Notes: “We use three low-cost webcams, no markers or specialized suits. This makes the system accessible in gyms, clinics, or even at home.”

## Slide 4
Engineering · EyobuNjineli · Ingenieurswese
System Architecture
Input: Multi-angle 2D video from 3 webcams
Notes: Input: ‘We capture synchronized video from 3 webcams.’

## Slide 5
Engineering · EyobuNjineli · Ingenieurswese
System Architecture
Processing: 5 pose estimation models tested (YOLOv8, OpenPose, etc.)
Notes: Processing: ‘We tested five state-of-the-art pose estimation models, including OpenPose and YOLOv8.’

## Slide 6
Engineering · EyobuNjineli · Ingenieurswese
System Architecture
Reconstruction: Stereo triangulation for 3D coordinates
Notes: Reconstruction: ‘2D keypoints from each camera are triangulated into 3D coordinates.’

## Slide 7
Engineering · EyobuNjineli · Ingenieurswese
System Architecture
Smoothing: Kalman filter for stability
Notes: Smoothing & Output: ‘We use a Kalman filter for stability, and visualize in real time using Unity.’

## Slide 8
Engineering · EyobuNjineli · Ingenieurswese
System Architecture
Output: Real-time Unity visualisation

## Slide 9
Engineering · EyobuNjineli · Ingenieurswese
Pose Estimation Model Performance
  Tested 5 state-of-the-art models
  Winner: YOLOv8m-pose
  Accuracy: 49.94mm mean error
  Speed: 32.10ms per frame (real-time capable) ≈ 30 FPS
    On Titan X (2015) GPU
  Best speed-accuracy trade-off
Notes: “We benchmarked five models. The winner: YOLOv8m-pose with ~50 mm mean error and 32 ms/frame latency. This gave the best speed–accuracy trade-off for real-time use.”

## Slide 10
Engineering · EyobuNjineli · Ingenieurswese
Real-Time System Design
  Web-cam system
  Camera calibration
  YOLOv8m-pose model generates 2D keypoints
  Triangulate 3D keypoints
Notes: Webcam system + calibration → YOLOv8 keypoints → triangulation.

## Slide 11
Engineering · EyobuNjineli · Ingenieurswese
Real-Time System Design
  Import 3D keypoints to Unity
  Construct segments
  Generate a full humanoid model
Notes: Unity builds the full humanoid model.

## Slide 12
Engineering · EyobuNjineli · Ingenieurswese
Real-Time System Performance
Notes: “In summary:
Low-cost webcams replace expensive lab systems.
~50 mm accuracy, real-time speed.
Provides immediate feedback for athletes. This work demonstrates how markerless AI-driven systems can make biomechanical training more accessible and scalable.”

## Slide 13
Engineering · EyobuNjineli · Ingenieurswese
Real-Time System Design
  Exercise Selection: 7 strength exercises supported
  Form Analysis: Joint angles, symmetry, alignment
  Real-Time Scoring: Performance metrics with colour coding
  Rep Counting: Automatic repetition detection
  Instant Feedback: Visual and numerical guidance
Notes: Exercises supported: 7 strength movements. We analyze joint angles, symmetry, and alignment, give scores and rep counts, and provide instant feedback.”

## Slide 14
Engineering · EyobuNjineli · Ingenieurswese
Real-Time System Design
Notes: “The system provides phase tracking, rep scores, and an overall movement score with colour-coded feedback. This mimics what a real trainer would highlight during a workout.”

## Slide 15
Engineering · EyobuNjineli · Ingenieurswese
  Action selection
  Full range of motion percentage
  Rep score
  Phase score
  Phase and rep tracking
  Segmented results
  Total movement score
1
2
3
4
5
6
7
Real-Time System Design
Notes: “The system runs real-time on standard hardware. Performance depends somewhat on video quality and lighting, but results are consistent within tested setups.”

## Slide 16
Engineering · EyobuNjineli · Ingenieurswese
  Video quality dependency
  Limited to tested exercises
  Need for broader population validation
Current Challenges
  Machine learning pose refinement
  Expanded exercise database
  Clinical validation studies
Future Directions
Limitations

## Slide 17
Engineering · EyobuNjineli · Ingenieurswese
  Cost-effective: Uses standard webcams instead of specialised equipment
  Performance: 50mm accuracy with 32ms processing speed per frame
  Immediate feedback: Real-time form correction and scoring
  Portable setup: Works in any environment with proper lighting
  User-friendly: No markers or technical expertise required
Key Takeaways
Notes: “Thank you for your attention. I’d be glad to take any questions.”

## Slide 18
Engineering · EyobuNjineli · Ingenieurswese
Acknowledgements
Lizé Steyn
Chris-Mari Schreuder
Notes: “Thank you for your attention. I’d be glad to take any questions.”

## Slide 19
Engineering · EyobuNjineli · Ingenieurswese
Thank you
Enkosi
Dankie
Notes: “Thank you for your attention. I’d be glad to take any questions.”

## Slide 20
Engineering · EyobuNjineli · Ingenieurswese
Real-Time System Performance
Notes: “Limitations: currently only tested on 7 exercises, depends on camera quality, and needs validation on a wider population. Future: refine machine learning models, expand the exercise library, and test in clinical/rehabilitation contexts.”

## Slide 21
Engineering · EyobuNjineli · Ingenieurswese
Movement Score Calculation
Notes: “Thank you for your attention. I’d be glad to take any questions.”